Patrick J. Murphy & Associates

Opus 59

St. Elizabeth Ann Seton Church

Carnegie, Pennsylvania

The organ of St. Elizabeth Ann Seton Church was built and installed in 2012 by Patrick J. Murphy & Associates of Stowe, Pennsylvania.  Consisting of 26 ranks over three manuals and pedal, the instrument is the firm’s Opus 59.   While the console, windchests, and mechanicals are all newly built, the organ contains both new and carefully selected, re-purposed pipework for color and quality.   Oak casework from the original St. Luke organ was retained, refurbished, and seamlessly integrated into the new case.  The organ, aided by a resonant acoustic, has already been proven an extremely capable liturgical and concert instrument.  The character of the instrument is warm, yet clear, with a predominance of eight foot tone.  The versatility and wide range of color available to the organist distinguish this instrument from many others its size.  Patrick J. Murphy Opus 59 will be formally dedicated by a series of concerts in 2012 and 2013.

Specification

Great

1.	16’ Bourdon (extension of #4)

2.	8’ Principal*

3.	8’ Diapason* (Ped)

4.	8’ Chimney Flute

5.	8’ Viola da Gamba (Sw)

6.	4’ Octave*

7.	4’ Hohlflute

8.	2’ Fifteenth

9.	V Fourniture

10.	16’ Bassoon (Sw)

11.	8’ Trumpet

Swell

12.	8’ Violin Diapason (borrowed from #16)

13.	8’ Stopped Diapason

14.	8’ Viola da Gamba

15.	8’ Viola Celeste t.c.

16.	4’ Principal

17.	4’ Harmonic Flute

18.	2 2/3’ Twelfth (borrowed form # 20)

19.	2’ Flautino

20.	1 1/3’ Nineteenth

21.	16’ Bassoon (extension of #23)

22.	8’ Trompette

23.	8’ Oboe

Tremolo

Solo

24.	8’ Chimney Flute (Gt)

25.	8’ Hohlflute (borrowed from #7)

26.	8’ Dulciana

27.	8’ Unda Maris t.c.

28.	4’ Chimney Flute (borrowed from #4)

29.	III Cornet g20-c49

30.	8’ Trumpet (Gt)

31.	8’ Clarinet

Tremolo

Pedal

32.	32’ Resultant

33.	16’ Open Diapason*

34.	16’ Bourdon

35.	8’ Diapason*

36.	8’ Bourdon

37.	4’ Super Octave*

38.	16’ Bassoon (Sw)

39.	16’ Posaune (extension of #11)

40.	8’ Trumpet (Gt)

41.	4’ Clarion (borrowed from #11)

Couplers

Gt—Gt 4’

Sw—Gt 16’

Sw—Gt 8’

Sw—Gt 4’

Solo—Gt 16’

Solo—Gt 8’

Solo—Gt 4’

Sw—Sw 16’

Sw—Sw 4’

Solo—Solo 16’

Solo—Solo 4’

Sw—Solo 16’

Sw—Solo 8’

Sw—Solo 4’

Gt—Ped 8’

Gt—Ped 4’

Sw—Ped 8’

Sw—Ped 4’

Solo—Ped 8’

*unenclosed stops

Great and Solo divisions under expression together

26 ranks total